## Slide 1: Feasibility Investigation on multicast broadcasting services in NB-iot ( based on 3GPP v14.0 )
Yunfeng Lu
MSS
Aug-18,2018

## Slide 2
General Procedures
Subscription
  a user establishes an agreement with the content provider to receive multicast broadcasting services
Service Announcement
  network to inform the devices about the offered services
Joining
  a device joins a multicast group before or during the multicast broadcasting service delivery
MS notification
  the network informs the devices about an imminent/ongoing service
Session start
  the network reserves the required resources
Data Transfer
  the period of time during which MBMS data is being transmitted
Session stop
  the network releases the allocated resources
Leaving
  User leaves a multicast services group

## Slide 3
char flows

## Slide 4
Entity
Subscription, joining and leaving are by per user basis
Session start /stop, data transfer and notification are based on per MS services

## Slide 5
Transmission mode
Single cell
  Each eNodeB send data to only devices in its cell,
  Transmission parameter configuration is independently from each eNodeB
Multi-cell
  a set of eNBs simultaneously transmit the same MBMS content
  The involved eNBs compose a single frequency network (SFN)
  e tightly synchronized in time and frequency to transmit the same data in the same frames/subframes and frequency resources.
  only the extended cyclic prefix may be used to avoid inter symbol interference

## Slide 6
Single cell – point to multipoint (SC-PTM) as 3GPP standard
Using two new channels
  SC-MCCH, single cell multicast control channel
  SC-MTCH, single cell multicast transport channel
  Scheduled in NPDCCH and transmitted in NPDSCH
  Control info is transmitted repeatedly with a period assigned by network
  Multicast data is identified by G-RNTI(group RNTI)
  A SC-MRB (single cell –multimedia radio bearer) is set up before session start and accessed by all devices in the group

## Slide 7
Frame structure of multicast channels
Multicast with fixed guarantee
Multicast with priority

## Slide 8
SC-MCCH info acquisition procedure
  NB-IoT UE that is receiving an MBMS service via SC-MRB may apply the SCMCCH information acquisition procedure, when
    upon receiving a notification that the SC-MCCH information is about to be changed due to start of a new service.
    upon receiving a notification that the SC-MCCH information that corresponds with the service that is being received is about to be changed
  Sc-MCCH info transmitted at frame of SFN mode m=0, configured by SystemInformationBlockType20-NB
  Multicast service occur only at idle period

## Slide 9
SC-MCCH information decoding
Start location of SC-MCCH info
  if [(H-SFN * 10240 + SFN * 10) + subframe number] modulo (SC-MCCH-SchedulingCycle) = SC-MCCHSchedulingOffset, begin to monitor NPDCCH with SC-RNTI in search space type-1A in SC-MCCH.
  if the PDCCH indicates a DL transmission, begin to decode NPDSCH to receive SCPTMConfiguration-NB message
DCI and Search space

## Slide 10
MTCH decoding
If a UE is configured by higher layers to decode NPDCCH with CRC scrambled by the G-RNTI, the UE shall decode the NPDCCH and the corresponding NPDSCH according to any of the combinations defined in Table 16.4.1-8. The scrambling initialization of NPDSCH corresponding to these NPDCCHs is by G-RNTI.
Start location of SC-MCCH information
  if [(H-SFN * 10240 + SFN * 10) + subframe number] modulo (SC-MCCH-SchedulingCycle) = SC-MCCHSchedulingOffset , begin to monitor NPDCCH with G-RNTI in search space type-2A in MTCCH.
  if the PDCCH indicates a DL transmission, begin to decode NPDSCH to receive data in MTCCH.

## Slide 11
DRX configuration in MCCH/MTCH
MCCH DRX configuration parameters:
  sc-mcch-onDurationTimerSCPTM
  sc-mcch-InactivityTimerSCPTM
  SC-MCCHSchedulingCycle
  SC-MCCH-SchedulingOffset
MTCH DRX configuration parameters:
  onDurationTimerSCPTM
  drx-InactivityTimerSCPTM
  the SC-MTCH-SchedulingCycle
  SC-MTCHSchedulingOffset

## Slide 12
SystemInformationBlockType20-NB-r14
SystemInformationBlockType20-NB-r14 ::= SEQUENCE {
npdcch-SC-MCCH-Config-r14 NPDCCH-SC-MCCH-Config-NB-r14,
sc-mcch-CarrierConfig-r14 DL-CarrierConfigCommon-NB-r14,
sc-mcch-RepetionPeriod-r14 ENUMERATED {rf32, rf128, rf512, rf1024,rf2048, rf4096, rf8192, rf16384},
sc-mcch-Offset-r14 INTEGER (0..10),
sc-mcch-ModificationPeriod-r14 ENUMERATED { rf32, rf128, rf256, rf512, rf1024,rf2048, rf4096, rf8192, rf16384, rf32768,rf65536, rf131072, rf262144, rf524288,rf1048576, spare1},
sc-mcch-SchedulingInfo-r14 SC-MCCH-SchedulingInfo-NB-r14,
lateNonCriticalExtension OCTET STRING OPTIONAL,
...
}

## Slide 13
RRC/MAC changes for multicast services
SC-PTM radio bearer configuration process
when
1)upon start of the MBMS session
2)upon entering a cell providing via SC-MRB a MBMS service in which the UE has interest
3)upon becoming interested in the MBMS service
call SC-MRB establishment process to start receiving a session of a MBMS services
when
1) upon stop of the MBMS session
2)upon leaving the cell where a SC-MRB is established
3)upon losing interest in the MBMS service
call SC-MRB release process to stop receiving a session
SC-MRB establishment process
1)configure SC-MTCH logical channel
2)configure physical layer with sc-mtch-InfoList IE
SC-MRB release process
1) release the RLC entity as well as the related MAC and physical layer configuration

## Slide 14: End of Presentation Thank you. Questions are welcome.