## Slide 1: Multicast services in NB-IOT
Yunfeng Lu, 2018.9

## Slide 2: Procedures
Subscription
  a user establishes an agreement with the content provider to receive MS services
Service Announcement
  network to inform the devices about the offered services
Joining
  a device joins a multicast group before or during the MS service delivery
MS notification
  the network informs the devices about an imminent/ongoing service
Session start
  the network reserves the required resources
Data Transfer
  the period of time during which MBMS data is being transmitted
Session stop
  the network releases the allocated resources
Leaving
  User leaves a multicast group

## Slide 3: Chart flows

## Slide 4: Entity
Subscription, joining and leaving are by per user basis
Session start , data transfer and notification are based on per MS services

## Slide 5: Transmission mode
Single cell
  Each eNodeB send data to only devices in its cell,
  Transmission parameter configuration is independently from each eNodeB
Multi-cell
  a set of eNBs simultaneously transmit the same MBMS content
  The involved eNBs compose a single frequency network (SFN)
  e tightly synchronized in time and frequency to transmit the same data in the same frames/subframes and frequency resources.
  only the extended cyclic prefix may be used to avoid inter symbol interference

## Slide 6: Single cell – point to multipoint (SC-PTM) as 3GPP standard
Using two new channels
  SC-MCCH, single cell multi-cast control channel
  SC-MTCH,
  Scheduled in NPDCCH and transmitted in NPDSCH
  Control info is transmitted repeatedly with a period assigned by network
  Multicast data is identified by G-RNTI(group RNTI)
  A SC-MRB (single cell –multimedia radio bearer) set up before session start and accessed by all devices in the group

## Slide 7: Frame structure of multicast channels
Multicast with fixed guarantee
Multicast with priority

## Slide 8: RRC/MAC changes to support multicast services
Radio bearers in RRC
DRX periods